## Slide 1: Drop Vertical Jumps to Assess Risk for Knee Degeneration and Future Total Knee Arthroplasty
Mentor: Nathan Schilaty
Group Members:
Eswar Kumar Katragadda
Juliana El Rayes
Vani Pailla

## Slide 2
OVERVIEW
06
04
03
Our Solution
Demonstration
01
Problem Statement
Q&A
02
Motivation
05
Next Steps

## Slide 3
PROBLEM STATEMENT
In a study done by our mentor, Dr. Nathan Schilaty, EMG and 3D motion capture data were collected during drop vertical jumps to study knee biomechanics. Due to a failed trigger signal, the data aren’t synchronized.
* EMG: Electromyography
Our focus is to align these datasets and create a synchronization method for EMG and motion capture data that enables accurate analysis of muscle and joint behavior during movement.

## Slide 4
MOTIVATION
Finding early signs of knee degeneration may help prevent surgeries like TKA.
Accurate sync between EMG and motion data is key for analysis.
How does aging affects muscle control and knee function?
Understanding Knee Degeneration
Need for Accurate Data Alignment
Early Detection
Our alignment work could enable meaningful comparisons of muscle and joint behavior.
Deeper Analysis
* TKA: Total Knee Arthroplasty

## Slide 5
TYPES OF JUMPS IN THE STUDY
DVJ
LSLL
Drop Vertical Jump
Left Single-Leg Landing
RSLL
CMJ
Right Single-Leg Landing
Countermovement Jump

## Slide 6
OUR SOLUTION
MATLAB script generated PNG plots of EMG signals for quick visual review.
MATLAB script allowed zoomed-in viewing to spot alignment features.
EMG .hpf and 3D motion .tak files were converted to .csv for processing.
Original Data
Live EMG Inspection
Batch EMG Plotting
Python script pulled start times from EMG .hpf files for synchronization.
UTC Extraction
Final Alignment
Python script matched EMG and motion data and split them into aligned jump trials.

## Slide 7
OUR SOLUTION
We were given EMG data as .csv files with varying column formats.
Script reads each file, finds the correct left and right Vastus Lateralis signals, and extracts them.
Generates side-by-side plots for left and right muscles.
Saves each plot as a high-resolution .png for visual inspection and pattern detection.
MATLAB Batch Plotting Script

## Slide 8
DEMOSTRATION
MATLAB Batch Plotting Script

## Slide 9
OUR SOLUTION
Allow us to interactively select and inspect individual EMG .csv files.
Plots full-duration signals for both left and right Vastus Lateralis muscles.
Also generates zoomed-in views of a specific time window.
Helps identify bursts, spikes, and other features for alignment.
MATLAB Live Script for Visual Inspection

## Slide 10
DEMOSTRATION
MATLAB Live Script for Visual Inspection

## Slide 11
OUR SOLUTION
Processes a folder of .hpf EMG files to extract UTC start times.
Uses regular expressions to find <StartTime> tags in file metadata.
Stores each filename and its timestamp in a summary .csv.
The timestamps support time-based alignment with motion capture data.
Python Script for UTC Timestamps

## Slide 12
DEMOSTRATION
Python Script for UTC Timestamps

## Slide 13
OUR SOLUTION
Uses extracted UTC start times from both EMG files and 3D motion capture .csv files.
Matches each EMG recording with the correct motion file based on timing.
Splits the motion data into individual jumps to align with EMG bursts.
Python Script for Final Alignment

## Slide 14
DEMOSTRATION
Python Script for Final Alignment

## Slide 15
NEXT STEPS SHORT-TERM
Verify Alignment Accuracy
Refine Alignment if Needed
Visual Comparison in MATLAB
Document the Workflow
Prepare Data for Statistical Analysis

## Slide 16
NEXT STEPS LONG-TERM
Feature Extraction
Clinical Relevance
Data Analysis or Modeling
Extract measurable metrics (e.g., onset time, activation peak) for statistical analysis.
01
02
03
Use aligned data to explore predictive modeling or pattern recognition.
With validation, this process could help support early detection tools for knee degeneration in a clinical or research setting.

## Slide 17
Q&A